## Slide 2: Basics
Fixed-point quantization （均匀量化）:
Power-of-2 quantization（非均匀量化）：
m: quantization bit
α: scaling factor

## Slide 3: Sum-of-Power-of-2 (SP2)
To address the non-negligible accuracy loss of power-of-2 quantization
q1,q2: power-of-2 numbers
m1+m2+1=m
m1≥m2
Levels:

## Slide 4: Sum-of-Power-of-2 (SP2)
ADDITIVE POWERS-OF-TWO QUANTIZATION: A NONUNIFORM
DISCRETIZATION FOR NEURAL NETWORKS ICLR’2020
Fixed-point Quantization:
  Suitable for Uniform-like weight distribution
  Can be implemented efficiently by DSP
SP2 Quantization:
  Suitable for Gaussian-like weight distribution
  Can be implemented efficiently by LUT

## Slide 5: Mixed scheme quantization (MSQ)
The distribution of the weights in the different rows are not the same.
To achieve better utilization of heterogeneous FPGA hardware resources.

## Slide 6: Mixed scheme quantization (MSQ)
Object detection
RNN model (NLP)

## Slide 7: FPGA Implementation
Four modules: Instruction, Load, Store, Compute
A hardware–software blueprint for flexible deep learning specialization Micro’2019

## Slide 8: FPGA Implementation
DSP: Fully utilized for conventional multiplication
LUT: Leveraged for computations with SP2 weights
Specifically, we progressively increase the size of GEMMsp2 core (Blkout;sp2), till the LUT utilization reaches 70%. For example, on XC7Z020 the desired fixed/SP2 ratio is 1:1.5 and on XC7Z045 it is 1:2

## Slide 9: FPGA Implementation
Throughput evaluation
Performance improvement: 2.1x-4.1x

## Slide 10: Conclusion
Software-Hardware co-design
A hardware-friendly quantization scheme: SP2
Intra-layer, multi-scheme quantization scheme: MSQ
Fully explore the FPGA resources
Performance improvement: 2.1x-4.1x